K BAR T Custom Homes, Inc.

# Customer Name:

# Address:

# Date:

Proposed Construction #:

## Home Site Improvements

Surveys

###### Homeowner to provide a site survey prior to starting foundation

Homeowner to provide final survey at completion of construction

##### Building Permits

Builder to provide all necessary building permits as per  		           County

## Utilities

###### Homeowner to provide electrical hook up by P.E.C.

Builder to provide electrical under ground up to 100 feet

## Sewage

Builder to provide septic design and septic installation as per    	               County

Builder to provide up to a maximum 4” sewer line up to 50 feet

## Water

## Homeowner to provide water well as per ______________ County

Builder to provide up to a maximum 2” water line up to 100 feet

## Foundation

Builder to provide engineered post tension foundation at 3000 psi

Note:	Foundation design engineered by MLAW Engineering

## Landscaping

Homeowner to provide landscaping and installation

### Homeowner Custom Specifications

#### Exterior Walls

Wood Frame: 	Lumber to be 2x4 @ 16” O.C.

Bottom Plate:	Lumber is to be treated 2x4 as per plan

Sheathing:	OSB and to be wrapped in Tyvek Builder Paper

Siding:		Hardi Plank located as per plan

Ceiling Framing

Joists:		2x6/2x8 as per plan

Roof Framing

Rafters:	as per plan

Ridges/ Hips 	as per plan

And Valleys

Roofing

Sheathing:	4x8x7/16” OSB with ply clips

Shingle:	Timberline 30 year dimensional shingle

Underlay:	#15 felt

Exterior Masonry

Home to be Hill Country Mix/ Austin Stone as per plan

Fireplace

Dry-Wall and Ceilings

Dry-wall to be ½”on all walls and 5/8” on ceilings

All walls to be taped, floated, and textured with a Monterey Drag

Insulation

Energy efficient with BIBS at exterior walls and R-38 blown in at attic

Foam/Caulking at windows, outside doors, plumbing pipes, and electrical wiring

Interior and Exterior Trim

Builder to install 5 1/4” baseboards (Colonial) as per plan

Folding attic stairway as per plan

All window sills to be wood

2X6 Dadoed to be used as fascia

Soffit to be 16” textured fiber cement

Hardi Plank to be used at Covered Patio

Note:  All trim to be paint grade

Interior and Exterior Doors

All interior doors to be Masonite hollow core doors (6x8”) as per plan

Builder to install front door as per plan ($1,500.00 allowance)

Interior and Exterior Door Hardware

Builder to install Oil Rubbed Bronze lever handles as per plan

Millwork

Builder to install Knotty Alder custom cabinetry as per plan

Interior and Exterior Painting

All walls and ceiling to be painted with Kelly Moore paint with a flat latex finish in color (1) of owner’s choice

All interior trim to be painted with Kelly Moore paint with a satin finish in color (1)

of owner’s choice

All exterior trim to be primed and painted with Kelly Moore paint in color (1) of owner’s

choice

Windows

All windows to be Vinyl, Double Paned, Low E, with Tan Frames as per plan

Flooring

Builder to install Tile Flooring as per plan

Builder to install Carpet as per plan

Heating and Air Conditioning

- 5 Ton Carrier/Lennox 14  SEER Heat Pump System

- R/A Outlet

- Set Refrigeration Line

- Set Drain Line

- Auxiliary Drain Pan

- Safety Float Switch for Auxiliary Drain Pan

- A/C Pad

- Honeywell Electronic Programmable Thermostat

- Control Wiring Only

- Dryer Vent

Note:  Duct Board 1 ½”, R-6 Flex, Mastic Seal, and Air Mate Grills

Note:	Tonnage may vary based on calculation loads

Electrical

Builder to provide the following:

1-	200 AMP Service

- 200 Amp Panel and Breakers

Plug Outlets included as per plan

Light Outlets included as per plan

Switch Outlets included as per plan (Rocker Panel)

Refrigerator Outlet included as per plan

Oven Outlet included as per plan

Microwave Outlet included as per plan

Disposal Outlet included as per plan

Dishwasher Outlet included as per plan

Washer Outlet included as per plan

Hot Water Outlet included as per plan

Air Handler Outlets included as per plan

A/C Outlets included as per plan

Fan Outlets included as per plan

TV Outlets as per plan

Phone Outlets as per plan

- Doorbell Outlet

Smoke Detector Outlets as per plan

Smoke Detectors as per plan

Recess cans as per plan

Eyeball Outlet as per plan

Garage Sconce Lighting as per plan

Electrical Fixtures

Homeowner to have 	$2,500		allowance to be installed as per plan

Plumbing

Kitchen:			Water to Refrigerator

Kitchen Sink:	Dayton 33x22 4hole 2 bowl stainless steel sink (under counter)

Kitchen Sink Faucet:	Delta lever kitchen faucet with spray (Oil Rubbed Bronze)

Master Bathroom Tub:	Soaker tub

Master Tub Faucet:	Delta 2 lever desk mount tub faucet (Oil Rubbed Bronze)

Master Shower:		Mud set shower pan with tile surround with seat

Master Shower Faucet:	Delta single lever faucet (Oil Rubbed Bronze)

Master Lavatory:		Granite countertops with drop in sinks

Master Lavatory Faucet:	2- Delta 2 lever 8” lavatory faucet (Oil Rubbed Bronze)

Master Bath Commode:	Vortens standard height elongated bowl commode (white)

Bath # 2 Tub/Shower:	Porcelain tub with tile surround

Bath # 2 Shower Faucet: 	Delta single lever tub and shower faucet (Oil Rubbed Bronze)

Bath #2 Lavatory:		Granite countertop with drop in sink (white)

Bath #2 Faucet:		Delta 2 lever 4” lavatory faucet (Oil Rubbed Bronze)

Bath #2 Commode:	Vortens standard height elongated bowl commode (white)

Water Heater (1):	Slate 40-gallon electric water heater

Outdoors:	4 Hose Bibbs

Note:	Preplumb for water softner system

Plumbing Fixtures

Builder to install Delta Oil Rubbed Bronze fixtures as per plan

Bathroom Mirrors

Homeowner to have standard mirrors installed as per plan

Note:	Beveled mirrors may incur additional investment

Kitchen Countertop, Bath 2 Countertop and Laundry

3cm Granite with a bullnosed edge

Tile back splash at kitchen as per plan

Note:	$46.50 allowance includes installation

Kitchen Appliances

Homeowner to have an allowance of     $4,000		         for the selection and installation of appliances as per plan

Final and Clean Up

Homesite shall be cleaned, construction debris removed and yard graded to slope from

residence

Builder expects completion time to be 8 months, but not more than 10  months.  Builder to provide Builder’s Risk Insurance during the construction process.  Change orders or item selected by customer which increase the cost of construction or exceed allowances specified in the Homeowner’s Custom Specifications or Plans shall be paid by customer at the time of the change or at construction completion.

Total Investment